## Slide 1: Bridge Pile Foundation Evaluation for a Soil Remediation Project
Will Tanner, P.E. Senior Engineer, Geosyntec Consultants, Inc.
Njoroge Wainaina, P.E., Senior Consultant, Geosyntec Consultants, Inc.

## Slide 2: Site Background
Railyard in Washington, DC
> 100-year history
Historic fueling operations result in plume of Diesel Range Organics (DRO’s)
I-295 elevated above tracks
  1957 original
  1988 expansion
Yard office construction and other improvements 2004
General Area of DRO Plume

## Slide 3: Site Background
Plume was intercepted by the installation of new stormwater infrastructure in 2004
Subsequent inadvertent DRO release to culvert junction area and adjacent creek
Immediate regulatory agency involvement
Commence plume delineation and Corrective Action Plan (CAP)
Creek

## Slide 4: Site Investigation
Environmental investigation to delineate extent of plume
4 I-295 Bridge Piers within the footprint
Geotechnical investigation
    4 Standard Penetration Test Borings
    4 Cone Penetration Tests (CPT’s) Soundings
Pier 10
Pier 11
Pier 9
Pier 8

## Slide 5: General Subsurface Profile
Very Still Clay
Silty Sand
Low Plasticity Clay
Silty Sand Fill
Very Still Clay
Silty Sand
Low Plasticity Clay
Silty Sand Fill

## Slide 6: I-295 Bridge Piers
Pier 10
Pier 8
Pier 11
Pier 9

## Slide 7: I-295 Bridge Piers & Proposed CAP
Several remedies considered
Excavation and Replacement
Approx 10-12 ft deep
5 ft offset from pile caps
Trans. Agency review and approval

## Slide 8: Load Estimation on Bridge Piers
AASHTO 2002 Standard
1957 Bridge Drawings and 1988 Expansion
Piers 8 and 10 have same configuration

## Slide 9: Load Estimation on Bridge Piers
AASHTO 2002 Standard
1957 Bridge Drawings and 1988 Expansion
Piers 9 and 11 have the same configuration

## Slide 10: Load Estimation on Bridge Piers (Summary)
Looking at 1988 pile caps directly adjacent to excavation
Max vertical Load = 800 kips
Max transverse (y-direction)
  Toward the excavation = 14 kips
Max parallel (x-direction)
  Direction of vehicular travel = 8 kips
Max overturning moment = 560 kip-ft
Wind directionality at 0 and 30 degree angles to bridge

## Slide 11: Pile Group Geometry and Load Distribution
Cast in place concrete piles
Independent groups
1988 group most affected
Loads distributed assuming cap is perfectly rigid
813 k
9 k
14 k
380 k-ft
460 k-ft

## Slide 12: Pile Group Geometry and Load Distribution
Cast in place concrete piles
Independent groups
1988 group most affected
Loads distributed assuming cap is perfectly rigid
840 k
9 k
15 k
421 k-ft
558 k-ft

## Slide 13: Pile Group Geometry and Load Distribution
Apply loads evenly across cap
Superposition
Rigid cap
PILEGRP
Resolve loads to single pile
Ready for Lpile!

## Slide 14: Lateral Load Analysis
Iterative finite difference computational approach implemented in Lpile
Use of pile-soil-pile modifiers to simulate group behavior
Two overall approaches
  Forward solution using resolved structural loads
  Inverse solution using target max. deflections of 0.25 inches (limit)

## Slide 15: Lateral Load Analysis
Selected p-y models
Parameters based on mix of lab data and literature values
Pile Properties
  12 in dia.
  “CIP” piles
  Resteel cage 4 #6’s
Reese Sand
Soft Clay
Stiff Clay
Reese Sand
D = 4ft
D = 16ft
D = 39ft
D = 73ft

## Slide 16: Lateral Load Analysis - Forward
Single pile analysis
P-multiplier = 0.7 (AASHTO 2010) for leading row
Pier 8 (x-direction)
  Axial load = 48.64 kips
  Lateral load = 0.46 kips
  Calculated deflection = 0.06 in.
Pier 9 (x-direction)
  Axial load = 50.58 kips
  Lateral load = 0.46 kips
  Calculated deflection = 0.02 in.

## Slide 17: Lateral Load Analysis – Inverse
Deflection threshold for entire group = 0.25 in
Pier 9
9 k applied

## Slide 18: Conclusions and Recommendations
Calculations demonstrated minor deflections are expected as a result of the excavation
Inverse analysis demonstrated that the load required to move an entire pile group 0.25 inches is an order of magnitude larger than the applied load
Both approaches indicated little concern
However the bridge structure is a critical part of DC traffic conveyance
Recommend pre and post construction condition assessments
Construction monitoring program

## Slide 19: Pre-Construction Condition Assessment

## Slide 20: Monitoring Program
Threshold value = 0.25 in
  If exceeded, increase frequency of monitoring
Limit value = 0.50 in
  Stop work if reached
  Notify agency
  Immediately place fill in excavation

## Slide 21: Construction
Excavation near Pier 9
Survey at Pier 9 pile cap

## Slide 22: Monitoring Program - Results
No discernable movement trends detected
System “noise” of about 0.15 inches
No threshold exceedance
No limiting value exceedance

## Slide 23: Post Construction Condition Assessment
No additional distress observed on the inspected bridge elements (piers, bearings, girders, decking, etc.)
Before
After

## Slide 24: Questions
Thank you!
Questions?